## Slide 1
Using Analytical Performance/Power Model and Fine-Grained DVFS to Enhance AI Accelerator Energy Efficiency
ASPLOS 2025
Zibo Wang1, Yijia Zhang2, Fuchun Wei3, Bingqiang Wang2, Yanlin Liu3, Zhiheng Hu3, Jingyi Zhang3,
Xiaoxin Xu3, Jian He3, Xiaoliang Wang1, Wanchun Dou1, Guihai Chen1, Chen Tian1
1Nanjing University 2Peng Cheng Laboratory 3Huawei
2025/7/14
Rotterdam, The Netherlands

## Slide 2
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion
Outline

## Slide 3
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 4
Introduction
Thermal Design Power(TDP) of AI Accelerators increases quickly.
V100
300 W
A100
400 W
H100
700 W
B100
~1000 W
Power usage of AI systems worldwide incurring high costs.
“Nvidia Sells over 1,500,000 H100 GPUs in 2024” from recent news
---equivalent to $1,200 million energy cost per year (if running at peak power)
Reducing energy consumption is necessary!

## Slide 5
Introduction
Our Goal:
To improve energy efficiency while keeping performance bounded!
Dynamic Voltage and Frequency Scaling (DVFS) is a main power control mechanism.
V↓ f↓ → Power↓ → Performance↓
V↑ f↑ → Power↑ → Performance↑
Limitation: Previous works apply DVFS at course granularity due to long DVFS latency(~15ms).
Opportunity:
  Performance impacts of DVFS vary across operators (Compute-bound👎🏻 Memory-bound👍🏻)
  Ascend NPU allows frequency adjustments for individual or multiple operators(~1ms).
Challenge: To set a frequency for every operator, search space is very large(>10k).
DVFS-based energy optimization for AI accelerators has been explored in many studies

## Slide 6
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 7
Overview
Profiling Data
Estimated Power
Estimated
Exec. Time
DVFS strategy
Power Model Construction
Perf. Model Construction
Generate
DVFS strategy
Estimated Energy
Performance Model: Operator cycle consumption follows a piecewise linear, convex function with AICore frequency.
Workload
Execute

## Slide 8
Overview
Profiling Data
Estimated Power
Estimated
Exec. Time
DVFS strategy
Power Model Construction
Perf. Model Construction
Generate
DVFS strategy
Estimated Energy
Performance Model: Operator cycle consumption follows a piecewise linear, convex function with AICore frequency.
Power Model: We incorporate the temperature factor often ignored by other works, improving the model's accuracy.
Workload
Execute

## Slide 9
Overview
Profiling Data
Estimated Power
Estimated
Exec. Time
DVFS strategy
Power Model Construction
Perf. Model Construction
Generate
DVFS strategy
Estimated Energy
Performance Model: Operator cycle consumption follows a piecewise linear, convex function with AICore frequency.
Power Model: We incorporate the temperature factor often ignored by other works, improving the model's accuracy.
Fine-Grained Frequency Control: By integrating operator classification, preprocessing, and a genetic algorithm-based search, we effectively reduce the search space and accelerate strategy optimization.
Workload
Execute

## Slide 10
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 11
Performance Model
AICore/SM
L1Cache
Compute Unit
L2Cache
HBM
Core Domain
Uncore Domain
The memory hierarchy our performance model relys on:
An L1 cache in each AICore
A shared L2 cache and High Bandwidth Memory (HBM)
Operating on different frequency domain

## Slide 12
Throughput (𝑇𝑝) of Ld/St is influenced by both the core frequency (𝑓) and the uncore bandwidth limitations:
Performance Model
Load/Store Bandwidth Analysis.
Assuming 𝑀 is the Ld/St data transfer volume and 𝑇 is its execution time:

## Slide 13
Performance Model
PingPong(Double Buffering)-Free and Independent Ld/St Scenarios.

## Slide 14
Performance Model
PingPong(Double Buffering)-Free and Independent Ld/St Scenarios.

## Slide 15
Performance Model
PingPong(Double Buffering)-Free and Independent Ld/St Scenarios.

## Slide 16
Performance Model
PingPong(Double Buffering)-Free and Independent Ld/St Scenarios.

## Slide 17
Summary of Performance Model
Insight:
The cycle count of an operator can be modeled as a convex piecewise linear function of frequency.
Challenge:
Unable to determine the breakpoints of the piecewise linear function.
Each data point requires a profiling process, so it is essential to minimize the amount of data needed for modeling to reduce the number of profiling runs.
Solution:
Employ commonly used concave function to fit the operator performance data.
Notes: For the other three scenarios, we can derive the function of the number of cycles consumed by the operator in relation to frequency in the same manner. We omit the detailed derivation here, but interested readers can refer to the paper for more details.
Through these analyses, we observe that the cycle count of an operator can be modeled as a convex piecewise linear function of frequency.
However, directly solving piecewise linear functions for each operator faces practical challenges:
It is impossible to identify the breakpoints since we have no methods to track the distribution of stalls within the core during operator execution.
Modeling requires running operators at different frequencies to collect performance data, yet each run consumes time and computational resources. Thus, minimizing the number of runs at different frequencies is crucial.
Given these limitation, we opt for a fitting approach to model the cycle count consumed by operators in relation to frequency and choose a quadratic functions without the linear term for fitting
𝑪𝒚𝒄𝒍𝒆(𝒇)&=𝒏×(𝒎𝒂𝒙(𝒂_𝟏 𝒇,𝒄_𝟏 )+𝒎𝒂𝒙(𝒂_𝟐 𝒇,𝒄_𝟐 )+𝑪𝒚𝒄𝒍𝒆(𝒄𝒐𝒓𝒆)+𝟐×𝑻_𝟎 𝒇)
𝑪𝒚𝒄𝒍𝒆(𝒇)&=𝒎𝒂𝒙(𝒂_𝟏 𝒇,𝒄_𝟏 )+𝒎𝒂𝒙(𝒂_𝟐 𝒇,𝒄_𝟐 )+𝑪𝒚𝒄𝒍𝒆(𝒄𝒐𝒓𝒆)+𝟐𝑻_𝟎 𝒇&+(𝒏−𝟏)×𝒎𝒂𝒙(𝒎𝒂𝒙(𝒂_𝟏 𝒇,𝒄_𝟏 )+𝑻_𝟎 𝒇, 𝒎𝒂𝒙(𝒂_𝟐 𝒇, 𝒄_𝟐 )+𝑻_𝟎 𝒇, 𝑪𝒚𝒄𝒍𝒆(𝒄𝒐𝒓𝒆))
𝑪𝒚𝒄𝒍𝒆(𝒇)&=𝒏/𝟐×(𝒎𝒂𝒙(𝒂_𝟏 𝒇,𝒄_𝟏 )+𝒎𝒂𝒙(𝒂_𝟐 𝒇,𝒄_𝟐 )+𝑪𝒚𝒄𝒍𝒆(𝒄𝒐𝒓𝒆))+𝒏𝑻_𝟎 𝒇&+𝒎𝒂𝒙(𝒎𝒂𝒙(𝒂_𝟏 𝒇,𝒄_𝟏 )+𝑻_𝟎 𝒇, 𝒎𝒂𝒙(𝒂_𝟐 𝒇, 𝒄_𝟐 )+𝑻_𝟎 𝒇, 𝑪𝒚𝒄𝒍𝒆(𝒄𝒐𝒓𝒆))

## Slide 18
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 19
Power Model
The dynamic power encompasses load-dependent power and load-independent power.
The static power can be decomposed into subthreshold leakage current and gate oxide current. Among them, the subthreshold leakage current can be considered to be linearly correlated with temperature ().
The hardware power consumption consists of dynamic power and static power.

## Slide 20
Power Model
Experiments reveal a linear correlation between AICore temperature 𝑇 and SoC power
Finally, we construct the power model through offline and online computation.
Relationship Between Temperature and SoC Power.
The Construction of a power model.

## Slide 21
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 22
Strategy Generation
Challenge:
When reducing energy consumption, minimizing performance loss is important
To set a frequency for each operator, search space is very large (>10k)
Solution:
Operator classification
Preprocessing and frequency point merging
Genetic algorithm-based search

## Slide 23
Strategy Generation
Operator classification: We categorize operators into two types: those sensitive to AICore frequency and those insensitive.
AICore Frequency-Sensitive Operators | Core-Bound, Latency-Bound operators
AICore Frequency-Insensitive Operators | Uncore-Bound, AICPU, communication operators and idle
Classification of operators based on their sensitivity to AICore frequency.

## Slide 24
Strategy Generation
Illustrations of each preprocessing step.
Preprocessing:
Gather the execution sequence and profiling data of operators
Analyse the bottleneck types
Devide the execution process into Low Frequency Candidate (LFC) and High Frequency Candidate (HFC)
Merge candidates with intervals shorter than a threshold with adjacent candidates

## Slide 25
Strategy Generation
Generation N, Individual 1
Generation N, Individual 2
Generation N, Individual 3
Using a genetic algorithm to search for different NPU operating frequency combinations to obtain the optimal energy-efficient configuration.
Generation N+1, Individual 1
Generation N+1, Individual 1
Generation N+1, Individual 1
Mutation
Crossover

## Slide 26
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 27
Evaluation
Testbed Introduction:
The Ascend NPU allows frequency adjustment with automatic voltage adaptation by its firmware.
It supports frequencies ranging from 1000MHz to 1800MHz in 100MHz increments.
Voltage-Frequency on Ascend NPU
Huawei Ascend

## Slide 28
Evaluation
Performance Model:
Workload: Over 5,000 operators across 6 frequency points, totaling over 30,000 data points.
We compare three different functions for fitting.
The one we use for fitting achieves an average prediction error of just 1.96%.
Error of predicted results of our Performance model

## Slide 29
Evaluation
Error of predicted results of our power model
Performance Model:
Workload: the training of GPT3, Bert, VGG19, ResNet50, ViT models, and Softmax and Tanh operators.
The model achieves an average prediction error of just 4.62% across multiple common workloads.

## Slide 30
Evaluation
End-to-End Experimental Results
Fine-Grained Frequency Scaling :
Workload: the training of GPT3, Bert, ResNet50 and ResNet152 with different performance loss target.
With a 2% performance loss target, an average performance loss of 1.76% achieves a 13.44% reduction in AICore energy consumption.

## Slide 31
Outline
Introduction
Overview
Performance Model
Power Model
Strategy Generation
Evaluation
Conclusion

## Slide 32
Conclusion
We optimize the end-to-end process of model training for energy efficiency.
We construct a white-box performance model with an average error of 1.96%.
We construct a power model incorporating a temperature-dependent factor, with an average error of 4.62%.
We propose a DVFS strategy for accelerators supporting millisecond-level DVFS control. Experiments demonstrate a reduction in AICore power by 13.44%, while limiting performance degradation to 1.76%.

## Slide 33
Thank you!
wangzb@smail.nju.edu.cn
ASPLOS 2025
2025/7/14
Rotterdam, The Netherlands